## Slide 1: A mathematical modeling for the stowage planning problem
Kiyoshi, TAKEDA
Yagiura lab

## Slide 2: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 3: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 4: Background
A carrier ship carries various loads through some ports.
We consider the ship that carries various type of cars. (e.g. passenger car, truck, bulldozer...)
Assignment of cars to ship is planned manually.
We aim to make assignment automatically

## Slide 5: Background
There are a lot of things that has to be considered
  Planning assignments that makes it easy to load and unload cars is important.
  Human error should not happen.
  Unbalanced assignments may result in a sinking.

## Slide 6: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 7: Problem Definition
We consider the ships which has 12 decks(floors).
Each deck has up to 4 holds
４
３
２
１

## Slide 8: Given definition
Order information

## Slide 9: Given information
Ship information
  How many holds exist.
  How large each hold is.
  Which holds are connected.
  etc…

## Slide 10: Stowage plan
We assign cars in every order to the hold.
  The order ID 0 is assigned the 3rd hold of 1st deck.
  The order ID 5 is assigned the 2rd hold of 4th deck.

## Slide 11: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 12: Mathematical Modeling
We model this assignment based on interviews with planners.
I and Mr.Ukawa made model for this assignment last year.
I will explain objective function and constraints one by one.

## Slide 13: The objective function
the objective function would be the weighted sum of the following five.
avoiding multiple orders in one hold
placing same orders by port closer together
securing a path to prevent loss of work efficiency
No dead space
placing empty space close to the entrance

## Slide 14: avoiding multiple orders in one hold
When an order is unloaded from a hold at a certain port, if there are several orders with different destinations in the same hold, human error may occur.
we minimize the number of orders with different destinations in different loading areas for each hold.
e.g. when unloading at port A
Port A
Port B
Port C
We add a penalty of two to the objective function

## Slide 15: placing same orders by port closer together
it is easy to load and unload cars if same orders by port are placed closer.
we minimize the number of orders with different ports that exist in adjacent pairs of holds.
        ○ ×
Port A
Port B
Port C
3rd floor
2nd floor
1st floor

## Slide 16: placing same orders by port closer together
As pair of adjacent holds, we consider two patterns
  Adjacent hold to the other
  Holds connected with a slope
We calculate the penalty for both loading ports and destination port
The penalty is 2
The penalty is 7
3rd floor
2nd floor
1st floor

## Slide 17: Securing a path to prevent loss of work efficiency
When a hold is full, it would be harder to pass through that hold.
The crew need to move cars in that hold once and bring them back again.
This leads to a loss of work efficiency.

## Slide 18: Securing a path to prevent loss of work efficiency
For each hold 𝑖, we define a filling rate that does not narrow the aisle of the car.
When loading 10 cars to hold 4:
  Red: the hold which the filling rate is exceeded.
  Blue: the hold which the filling rate is not exceeded.
Total penalty for this situation is 20 (10 *2)
1
2
3
4

## Slide 19: No dead space
There are some holds with a ramp connecting the deck to the deck.
Once these holds are filled to a certain extent, it will be impossible to reach the deeper holds.
  This space is called “dead space”
We minimize the number of dead space.
90% full
60% full
50% full
60% full
These space are called dead space

## Slide 20: placing empty space close to the entrance
It often happens that orders are added just before the voyage.
To handle that situation, we should place empty space close to the entrance
The entrance

## Slide 21: placing empty space close to the entrance
The ship has 12 floors and the entrance is on the 5th floor.
If there are lots of empty space in the 5th floor’s holds, we get more profit.
We subtract that profit from the objective function.

## Slide 22: Constraints
There are 3 constraints in making assignment.
Travel routes in the ship
Weight balance of cargo
All vehicles must be loaded.

## Slide 23: Travel paths in the ship
we secure a path for cars to be able to pass.
For each hold i, we define
  the current filling rate as
  the maximum filling rate that a car can pass as
After loading all vehicles at each port except the last port,

## Slide 24: Weight balance of cargo
When the ship tilts, there is a possibility that the ship will lose its balance and roll over.
we add constraints for balance in two directions
  Forward and backward direction
  Vertical direction

## Slide 25: Forward and backward direction
For each hold 𝑖, we define a coefficient
  Positive coefficient from center to forward hold
  negative coefficient from center to back hold
The closer the center of gravity is to zero in the forward and backward directions, the more stable the ship will be.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 26: Vertical direction
For each hold 𝑖, we define a coefficient
  Positive coefficient for the hold above sea level
  negative coefficient for the hold below sea level
The farther away from the sea surface, the greater the effect is.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 27: Computational experiment
With this model, we confirmed that we can get a good assignment for small bookings.
The number of orders and the number of loading and unloading ports increases, the calculations may not be sufficiently advanced in a limited time.[1]
[1]鵜川知哉, 自動車運搬船における貨物積載プラン ニングの席割問題に対する数理モデリング, 修士 論文，名古屋大学情報学研究科, 2020

## Slide 28: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 29: Different model
We propose different model to solve large bookings.
We'll call this model “the 2nd model”.
The basic idea is based on heuristics.
Using the local search, we improve the assignment

## Slide 30: Detailed Heuristic
In the 1st model, continuous numbers of units were used as variables.
In the 2nd model, instead of assigning each unit individually, we split the orders and assign them.
As for holds, we think about grouping some holds together and assigning orders to them.
  We call them “segment”.

## Slide 31: Detailed Segment
The ship has 43 holds.
We divide them into 17 segments.
It is based on the rule that on each floor, planners assign the cars in order from the back hold to the hold with the ramp.
this grouping enable the model to create assignment that is similar to planners'.

## Slide 32: Detailed Segment
→

## Slide 33: Comparison of the two models
1st model
assigning 35 vehicles of order 1 to 3rd hold of 4th deck.
same as real operations.
2nd model
Assigning order 1 to 3rd segment
Once assignments are decided, we load vehicles from the back according to the rules.

## Slide 34: Rules for loading vehicles
The vehicles of the orders assigned to each segment are loaded from the back hold.
We want to load the vehicle while satisfying the constraints.

## Slide 35: Constraints that has to be satisfied when loading
We load vehicles while satisfying the following travel routes constraints.
We ensure that the filling rate is not exceeded after all vehicles have been loaded at a particular port.
Other constraints or objectives are calculated in the evaluation function.

## Slide 36: Local Search
moving from solution to solution in the space of candidate solutions by applying local changes
We repeat this operation until the termination condition is satisfied
In this research, we use shift neighborhood and swap neighborhood

## Slide 37: Evaluate function
As the evaluation function used to find the solution, we use the weighted sum of the constraint and the objective function.
constraint
Travel routes in the ship
Weight balance of cargo
All vehicles must be loaded.
Objective function
avoiding multiple orders in one hold
placing same orders by port closer together
securing a path
No dead space
placing empty space close to the entrance

## Slide 38: Neighborhood
Shift neighborhood
  This is obtained by reassigning one order which was assigned to a segment to another segment
Swap neighborhood
  This is obtained by swapping the allocated segments of two orders.

## Slide 39: Flow of local search
searching the shift neighborhood until no better solution is found.
searching the swap neighborhood until no better solution is found.
If better solution is found in step 1 or step 2, return to step 1.

## Slide 40: Swap neighborhood
We swap the two orders assigned to different segments.
ex. array of orders in each segment are as follows:
Segment 1 segment 2
[A,B,C,D] [E,F,G,H]
Segment 1 segment 2
[A,B,F,D] [E,C,G,H]

## Slide 41: Shift neighborhood
We select one order assigned to a segment and reassign it to a different segment.
ex. array of orders in each segment are as follows:
Segment 1 Segment 2
[A,B,C,D] [E,F,G,H]
Segment 1 Segment 2
[A,B,D] [E,F,G,C,H]

## Slide 42: Shift neighborhood
When searching shift neighborhoods, we normally calculate the evaluate function for all possible insertion positions and insert in the best position.
For this problem, there may be a waste of resources.

## Slide 43: Waste of resources in the neighborhood
When inserting one order into another hold, we make a change in the order sequence of the orders to be inserted.
Example: inserting order A
[C,B,D] → [A, C, B, D]
[C, A, B, D]
[C, B, A, D]
[C, B, D, A]
In this case, we try 4 patterns and select the best inserted position.

## Slide 44: Waste of resources in the neighborhood
Some insertions may result in the exact same assignment.
Ex. when this segment has 2 holds(:
In this case, trying 2 patters is enough.
Pattern | insertion | orders in hold | orders in hold
1 | A, C, B, D | A,C | B,D
2 | C, A, B, D | C,A | B,D
3 | C, B, A, D | C,B | A,D
4 | C, B, D, A | C,B | D,A
Pattern | insertion |  | 
1 | A, C, B, D | A,C | B,D
2 | C, A, B, D | C,A | B,D
3 | C, B, A, D | C,B | A,D
4 | C, B, D, A | C,B | D,A

## Slide 45: Our approach to reduce the number of insertions
We propose an approach to reduce the number of insertions.
We insert it at the end of the order sequence.
we memorize orders that are split in two.
We insert only in adjacent parts of split orders.
We select the best insertion position

## Slide 46: Our approach to reduce the number of insertions
When inserting order A to segment with the following order sequence:
B, C, D, E, F, G, H, I, J
1. We insert order A to the sequence in the end
B, C, D, E, F, G, H, I, J, A
2. We memorize orders that are split in two.
In this case, we insert only before and after order F, and select the best insertion position.
insertion | hold | Hold
B, C, D, E, F, G, H, I, J, A | B, C, D, E, F | F, G, H, I, J, A
insertion |  | 
B, C, D, E, F, G, H, I, J, A | B, C, D, E, F | F, G, H, I, J, A

## Slide 47: Our approach to reduce the number of insertions
instance |  |  | Inserting all positions | Our approach
Num of orders | Num of L ports | Num of D ports | Computation time | Computation time
109 | 2 | 3 | 145 | 81
109 | 2 | 5 | 192 | 89
109 | 4 | 3 | 122 | 99
250 | 2 | 3 | 387 | 204
We compare our approach with inserting all the possible position.
We confirmed that we can reduce the computation time while keeping the quality of solutions

## Slide 48: Comparison by insertion method
The computation time could be reduced; however, it would take some time.
We have compared the quality and the computation time for the following two cases:
Case that orders are inserted into the optimal position based on our approach
Case that orders are inserted randomly

## Slide 49: Our approach to reduce the number of insertions
instance |  |  | inserting to the best position |  | inserting randomly | 
Num of orders | Num of L ports | Num of D ports | value | Computation time | value | Computation time
109 | 2 | 3 | -2533 | 2244 | -2975 | 873
109 | 2 | 5 | -1492 | 5051 | -1167 | 938
109 | 4 | 3 | -144 | 4965 | -1378 | 728
250 | 2 | 3 | -2925 | 7275 | -2235 | 3069

## Slide 50: Comparison by insertion method
Computation time varies greatly.
The quality of the local optimal solution is not very different between the two approaches.
When this algorithm is actually used, it will be checked by a person in the end.
there may be possibilities that obtaining a solution with a certain degree of quality in a short time may be sufficient.

## Slide 51: Initial solution
We propose several approach to create initial assignment.
generating from solution by relaxation of linear programming
Generating from solution of a problem formulated in MIP with orders grouped by port

## Slide 52: Approach to create initial assignment
generating from solution by relaxation of linear programming
Generating from solution of a problem formulated in MIP with orders grouped by port

## Slide 53: Relaxation of linear programming
As a preliminary experiment, we compare the solutions to the MIP problem and the relaxation problem.
To compare the properties of the solutions, we use the Hamming distance.
For vectors x and y, we define the Hamming distance as follows.

## Slide 54: Example of Hamming distance
We consider the following conditions
  The number of orders is 3 and the number of holds is 4.
  Each order contains 100 vehicles.
The values of the vectors take a small number between 0 and 1.
  the value is 1 when allocating 100% of the order
  the value is 0.5 when allocating 50% of the order

## Slide 55: Example of Hamming distance
We consider the situation that each order contains 100 vehicles.
→
we convert the values as shown in this table
order
hold
 | 1 | 2 | 3 | 4
A | 30 | 70 | 0 | 0
B | 0 | 0 | 100 | 0
C | 10 | 10 | 0 | 80
 | 1 | 2 | 3 | 4
A | 0.3 | 0.7 | 0 | 0
B | 0 | 0 | 1.0 | 0
C | 0.1 | 0.1 | 0 | 0.8

## Slide 56: Example of Hamming distance
Pattern 1
Pattern 2
1.6
0
0.4
1.6
0
0.4
 | 1 | 2 | 3 | 4
A | 0.3 | 0.7 | 0 | 0
B | 0 | 0 | 1.0 | 0
C | 0.1 | 0.1 | 0 | 0.8
 | 1 | 2 | 3 | 4
A | 0.2 | 0 | 0.8 | 0
B | 0 | 0 | 1.0 | 0
C | 0.2 | 0.2 | 0 | 0.6
|0.3-0.2|+|0.7-0|+|0-0.8|
Total distance: 2.0
For each order i, The sum of would be 1.0 and The maximum total distance will be twice the number of orders.
By dividing by twice the number of orders, we can see how different the solutions are.
(In this case, 33%)

## Slide 57: Result of Hamming distance
orders | L ports | D ports | Difference(%)
38 | 2 | 3 | 0.19
63 | 2 | 3 | 3.57
57 | 2 | 5 | 1.07
66 | 4 | 3 | 0.71
We performed the comparison only on instances for which we had the exact best solution.
we confirmed that the properties of the relaxed solution and the MIP solution are close for all instances.

## Slide 58: Rounding the relaxed solution
For every orders, the value of the variable assigned to the hold is used as a probability to randomly determine which hold to assign to.
If the capacity constraint of the hold is not satisfied, we will not assign orders to that hold.
Hold | Value of the relaxed solution.
A | 0.2
B | 0.5
C | 0.3
Hold | Probability that orders are assigned
A | 20%
B | 50%
C | 30%

## Slide 59: Approach to create initial assignment
generating from solution by relaxation of linear programming
Generating from solution of a problem formulated in MIP with orders grouped by port

## Slide 60: MIP with orders grouped by port
I and Mr.Ukawa proposed a model that combines orders with the same loading and unloading ports into a single order to create an assignment.
With this model, we can get assignments in a short computation time.
[1]鵜川知哉, 自動車運搬船における貨物積載プラン ニングの席割問題に対する数理モデリング, 修士 論文，名古屋大学情報学研究科, 2020

## Slide 61: MIP with orders grouped by port
We received a comment that the assignment cannot not actually be used and needed to be modified.
We propose to use the assignment as an initial solution and then perform local search to modify it.
I haven’t finished implementing yet…

## Slide 62: Comparison by initial solution
instance | randomly generated |  | Relaxation solution | 
 | Value | Computation time (seconds) | Value | Computation time (seconds)
109-2-3 | -2975 | 873 | -2179 | 1641
109-2-5 | -1167 | 938 | -594 | 8057
109-4-3 | -1378 | 728 | 1840 | 8782
250-2-3 | -2235 | 3069 | -2755 | 9726
Instance name:
number of orders- number of loading port- number of unloading port

## Slide 63: Comparison by initial solution
For large instances, it takes a long time to find a solution, even for a relaxation problem.
In terms of computation time, a randomly generated solution may be effective.

## Slide 64: Computational experiment
We compare the computation time and the quality of assignment.
For 1st model, we show the values of the solution after 1 hour and after 24 hours
For 2nd model, we show the value of the solution and the computation time to finish the local search.

## Slide 65: Comparison of two models
instance | 1st model |  | Our best approach | 
 | Value after 3600s | Value after 86400s | Value | Computation time (seconds)
109-2-3 | -508 | -3478 | -2975 | 873
109-2-5 | -2612 | -3354 | -1167 | 938
109-4-3 | 1240 | -3455 | -1378 | 728
250-2-3 | infeasible | -2064 | -2235 | 3069
we get feasible solutions with a certain quality in a relatively short computation time.
Instance name:
number of orders - number of loading port - number of unloading port

## Slide 66: Computational experiment
 |  |  | 1st model |  | 2nd model | 
Num of orders | Num of L ports | Num of D ports | Value after 1h (3600s) | Value after 24h (86400s) | Value | Computation time (seconds)
109 | 2 | 3 | -508 | -3478 | -2975 | 873
109 | 2 | 5 | -2612 | -3354 | -1167 | 938
109 | 4 | 3 | 1240 | -3455 | -1378 | 728
250 | 2 | 3 | infeasible | -2064 | -2235 | 3069
200 | 2 | 3 | infeasible | -840 | infeasible | 6481
350 | 2 | 3 | infeasible | 3726 | infeasible | 19219

## Slide 67: Summary &future work
Summary
  We proposed model which is based on heuristic.
  In a relatively short computation time, we got feasible solutions with a certain quality.
Future work
  Finishing implementing an approach to use MIP solution to create initial solution