## Slide 1: A local search algorithm for the stowage planning problem for pure car carrier ships
Kiyoshi TAKEDA
Yagiura lab

## Slide 2: Outline
Background
Problem definition
Proposed model
Summary

## Slide 3: Outline
Background
Problem definition
Proposed model
Summary

## Slide 4: Background
A carrier ship carries various loads through some ports.
Assignment of cars to ship is planned manually.
We aim to make assignment automatically

## Slide 5: Background
There are a lot of things that has to be considered
  Planning assignments that makes it easy to load and unload cars is important.
  Human error should not happen.
  Unbalanced assignments may result in a sinking.

## Slide 6: Outline
Background
Problem definition
Proposed model
Summary

## Slide 7: Problem Definition
We consider a ship that has 12 decks (floors).
Each deck has up to 4 holds
４
３
２
１

## Slide 8: Given definition
We are given information on bookings.
  Booking ID
  Loading port
  Destination port
  Number of vehicles
  Size of vehicles
  etc…

## Slide 9: Given information
We are also given information about ships.
  How many holds exist.
  How large each hold is.
  Which holds are connected.
  etc…

## Slide 10: Stowage Plan
ID | L-Port | D-Port | Number
1 | Port A | Port C | 5
2 | Port A | Port D | 8
2 | Port B | Port D | 5
Booking
Stowage Plan
ID | Floor | Hold | Number
1 | 1st | 1 | 2
1 | 1st | 2 | 3
2 | 2nd | 3 | 4
2 | 2nd | 1 | 5
3 | 3rd | 2 | 2
3 | 3rd | 3 | 3

## Slide 11: Mathematical Modeling
We conducted multiple interviews with the planners who actually decide the stowage plan.
We model this assignment based on interviews.
I will explain objective function and constraints one by one.

## Slide 12: The objective function
The objective function is the weighted sum of the following five.
avoiding multiple bookings in one hold
placing same bookings by port closer together
securing a path to prevent loss of work efficiency
No dead space
placing empty space close to the entrance

## Slide 13: avoiding multiple bookings in one hold
When a booking is unloaded from a hold at a certain port, if there are several bookings with different destinations in the same hold, human error may occur.
we minimize the number of bookings with different destinations in different loading areas for each hold.
○
×

## Slide 14: placing same bookings by port closer together
it is easy to load and unload cars if same bookings by port are placed closer.
we minimize the number of bookings with different ports that exist in adjacent pairs of holds.
○ ×
Port A
Port B
Port C

## Slide 15: Securing a path to prevent loss of work efficiency
When a hold is full, it would be harder to pass through that hold.
The crew need to move cars in that hold once and bring them back again.
This leads to a loss of work efficiency.

## Slide 16: No dead space
There are some holds with a ramp connecting the deck to the deck.
Once these holds are filled to a certain extent, it will be impossible to reach the deeper holds.
  This space is called “dead space”
We minimize the number of dead space.
These space are called dead space

## Slide 17: placing empty space close to the entrance
It often happens that bookings are added just before the voyage.
To handle that situation, we should place empty space close to the entrance

## Slide 18: Constraints
There are 3 constraints in making assignment.
Travel routes in the ship
Weight balance of cargo
All vehicles must be loaded.

## Slide 19: Travel paths in the ship
we secure a path for cars to be able to pass.
For each hold i, we define
  the current filling rate as
  the maximum filling rate that a car can pass as
After loading all vehicles at each port except the last port,

## Slide 20: Weight balance of cargo
When the ship tilts, there is a possibility that the ship will lose its balance and roll over.
we add constraints for balance in two directions
  Forward and backward direction
  Vertical direction

## Slide 21: Outline
Background
Problem definition
Proposed model
Summary

## Slide 22: Modeling
We propose mathematical model to this problem.
The basic idea is based on heuristics.
Using the local search, we improve the assignment.

## Slide 23: Modeling
We propose model that splits the bookings and assigns them to holds.
As for holds, we think about grouping some holds together and assigning bookings to them.
  We call them “segment”.

## Slide 24: Segment
The ship has 43 holds.
We divide them into 17 segments.
It is based on the rule that on each floor, planners assign the cars in order from the back hold to the hold with the ramp.
this grouping enable the model to create assignment that is similar to planners'.

## Slide 25: Detailed Segment
→

## Slide 26: Expression of solution
As a solution, we store an array whose elements are a set of bookings.
The number of array is the number of segments.
The th element represents the set of bookings that will be assigned to the -th segment.

## Slide 27: Expr ession of solution
e.g.
The -th segment is a combination of hold and hold .
Bookings that will be assigned to the -th segment are
[A,B,C,D,E,F,G,H]
For example, the assignment to each hold can be as follows:
  hold → bookings A,B,C
  hold → booking D,E,F,G,H

## Slide 28: Expr ession of solution
Each booking has a different number of vehicles.
If the sequence of arrays changes, the bookings assigned to the holds may change.
e.g.
[A,B,C,D,E,F,G,H] [A,B,E,F,C,D,G,H]
hold →A, B, C, D hold → A, B, E
hold →E, F, G, H hold → F, C, D, G, H

## Slide 29: Assigning to hold
Given an array of booking assigned to segments, we assign the bookings to holds based on the rules.
We load the vehicles from the back hold while satisfying the travel routes constraints.
Other constraints or objectives are calculated in the evaluate function.

## Slide 30: Local Search
moving from solution to solution in the space of candidate by applying local changes
We repeat this operation until the termination condition is satisfied
In this research, we use shift neighborhood and swap neighborhood.

## Slide 31: Neighborhood
Shift neighborhood
  This is obtained by reassigning one booking which was assigned to a segment to another segment.
Swap neighborhood
  This is obtained by swapping the allocated segments of two bookings.

## Slide 32: Flow of local search
searching the shift neighborhood until no better solution is found.
searching the swap neighborhood until no better solution is found.
If better solution is found in step 1 or step 2, return to step 1.

## Slide 33: Shift neighborhood
When searching shift neighborhoods, we normally calculate the evaluate function for all possible insertion positions and insert in the best position.
For this problem, there may be a waste of resources.

## Slide 34: Waste of resources in the neighborhood
When inserting one booking into another hold, we make a change to the sequence order of the bookings to be inserted.
Example: inserting booking A
[C,B,D] → [A, C, B, D]
[C, A, B, D]
[C, B, A, D]
[C, B, D, A]
In this case, we try 4 patterns and select the best inserted position.

## Slide 35: Waste of resources in the neighborhood
Some insertions may result in the exact same assignment.
e.g. when this segment has 2 holds(:
In this case, trying 2 patters is enough.
Pattern | insertion | bookings in hold | bookings in hold
1 | A, C, B, D | A,C | B,D
2 | C, A, B, D | C,A | B,D
3 | C, B, A, D | C,B | A,D
4 | C, B, D, A | C,B | D,A
Pattern | insertion |  | 
1 | A, C, B, D | A,C | B,D
2 | C, A, B, D | C,A | B,D
3 | C, B, A, D | C,B | A,D
4 | C, B, D, A | C,B | D,A

## Slide 36: Our approach to reduce the number of insertions
We propose an approach to reduce the number of insertions.
We insert it at the end of the booking sequence.
we memorize bookings that are split in two.
We insert only in adjacent parts of split bookings.
We select the best insertion position

## Slide 37: Our approach to reduce the number of insertions
When inserting booking A to segment with the following order sequence:
B, C, D, E, F, G, H, I, J
1. We insert booking A at the end of the sequence.
B, C, D, E, F, G, H, I, J, A
2. We memorize booking that are split in two.
In this case, we insert only before and after booking F, and select the best insertion position.
insertion | hold | Hold
B, C, D, E, F, G, H, I, J, A | B, C, D, E, F | F, G, H, I, J, A
insertion |  | 
B, C, D, E, F, G, H, I, J, A | B, C, D, E, F | F, G, H, I, J, A

## Slide 38: Our approach to reduce the number of insertions
instance |  |  | Inserting all positions | Our approach
Number of orders | Number of L ports | Number of D ports | Computation time | Computation time
109 | 2 | 3 | 145 | 81
109 | 2 | 5 | 192 | 89
109 | 4 | 3 | 122 | 99
250 | 2 | 3 | 387 | 204
We compare our approach with inserting all the possible position.
We confirmed that we can reduce the computation time while keeping the quality of solutions

## Slide 39: Initial solution
Approaches we propose to create initial solutions:
generating from solution by relaxation of linear programming
generating from solution of a problem formulated in MIP with bookings grouped by port

## Slide 40: Approach to create initial assignment
generating from solution by relaxation of linear programming
Generating from solution of a problem formulated in MIP with bookings grouped by port

## Slide 41: Relaxation of linear programming
As a preliminary experiment, we compare the solutions to the MIP problem and the relaxation problem.
To compare the properties of the solutions, we use the Manhattan distance.
We performed the comparison and confirmed that the properties of the relaxed solution and the MIP solution are close.

## Slide 42: Approach to create initial assignment
generating from solution by relaxation of linear programming
Generating from solution of a problem formulated in MIP with bookings grouped by port

## Slide 43: MIP with bookings grouped by port
We propose using a solution of a model that combines bookings with the same loading port and unloading port into a single booking to create an assignment.
With this approach, we can get a rough solution in a short time.

## Slide 44: Comparison by initial solution
instance | randomly generated |  | relaxation solution |  | bookings grouped by port | 
 | Value | Computation time (seconds) | Value | Computation time (seconds) | Value | Computation time (seconds)
109-2-3 | -2975 | 873 | -2179 | 1641 | -2896 | 776
109-2-5 | -1167 | 938 | -594 | 8057 | -3247 | 2650
109-4-3 | -1378 | 728 | 1840 | 8782 | -1873 | 3009
250-2-3 | -2235 | 3069 | -2755 | 9726 | -3476 | 1605
Instance name:
number of orders- number of loading port- number of unloading port

## Slide 45: Computational experiment
We compare the quality and the computation time of the proposed model with that of solving MIP problem.
For MIP problem, we show the values of the solution after 1 hour and after 24 hours
For proposed model, we show the value of the solution and the computation time to finish the local search.

## Slide 46: Comparison of two models
instance | Solving MIP |  | Our best approach | 
 | Value after 3600s | Value after 86400s | Value | Computation time (seconds)
109-2-3 | -508 | -3478 | -2896 | 776
109-2-5 | -2612 | -3354 | -3247 | 2650
109-4-3 | 1240 | -3455 | -1873 | 3009
250-2-3 | infeasible | -2064 | -3476 | 1605
Instance name:
number of orders - number of loading port - number of unloading port

## Slide 47: Summary
We formulated the stowage planning problem and proposed model which is based on heuristic.
we propose an approach to reduce computation time in local search.
We propose 2 approach to generate initial solution.
We confirmed that we can get feasible solutions with a certain quality in a relatively short computation time.

## Slide 48: supplementary materials

## Slide 49: avoiding multiple bookings in one hold
When a booking is unloaded from a hold at a certain port, if there are several bookings with different destinations in the same hold, human error may occur.
we minimize the number of bookings with different destinations in different loading areas for each hold.
e.g. when unloading at port A
Port A
Port B
Port C
We add a penalty of two to the objective function

## Slide 50: placing same bookings by port closer together
it is easy to load and unload cars if same bookings by port are placed closer.
we minimize the number of bookings with different ports that exist in adjacent pairs of holds.
○ ×
Port A
Port B
Port C
The penalty is 2
The penalty is 7

## Slide 51: Securing a path to prevent loss of work efficiency
For each hold 𝑖, we define a filling rate that does not narrow the aisle of the car.
When loading 10 cars to hold 4:
  Red: the hold which the filling rate is exceeded.
  Blue: the hold which the filling rate is not exceeded.
Total penalty for this situation is 20 (10 *2)
1
2
3
4
entrance

## Slide 52: placing empty space close to the entrance
The ship has 12 floors and the entrance is on the 5th floor.
If there are lots of empty space in the 5th floor’s holds, we get more profit.
We subtract that profit from the objective function.

## Slide 53: Forward and backward direction
For each hold 𝑖, we define a coefficient
  Positive coefficient from center to forward hold
  negative coefficient from center to back hold
The closer the center of gravity is to zero in the forward and backward directions, the more stable the ship will be.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 54: Vertical direction
For each hold 𝑖, we define a coefficient
  Positive coefficient for the hold above sea level
  negative coefficient for the hold below sea level
The farther away from the sea surface, the greater the effect is.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 55: Shift neighborhood
We select one order assigned to a segment and reassign it to a different segment.
ex. array of orders in each segment are as follows:
Segment 1 Segment 2
[A,B,C,D] [E,F,G,H]
Segment 1 Segment 2
[A,B,D] [E,F,G,C,H]

## Slide 56: Swap neighborhood
We swap the two orders assigned to different segments.
ex. array of orders in each segment are as follows:
Segment 1 segment 2
[A,B,C,D] [E,F,G,H]
Segment 1 segment 2
[A,B,F,D] [E,C,G,H]

## Slide 57: Evaluate function
As the evaluation function used to find the solution, we use the weighted sum of the constraint and the objective function.
constraint
Travel routes in the ship
Weight balance of cargo
All vehicles must be loaded.
Objective function
avoiding multiple orders in one hold
placing same orders by port closer together
securing a path
No dead space
placing empty space close to the entrance

## Slide 58: Comparison by insertion method
The computation time could be reduced; however, it would take some time.
We have compared the quality and the computation time for the following two cases:
Case that orders are inserted into the optimal position based on our approach
Case that orders are inserted randomly

## Slide 59: Our approach to reduce the number of insertions
instance |  |  | inserting to the best position |  | inserting randomly | 
Num of orders | Num of L ports | Num of D ports | value | Computation time | value | Computation time
109 | 2 | 3 | -2533 | 2244 | -2975 | 873
109 | 2 | 5 | -1492 | 5051 | -1167 | 938
109 | 4 | 3 | -144 | 4965 | -1378 | 728
250 | 2 | 3 | -2925 | 7275 | -2235 | 3069

## Slide 60: Comparison by insertion method
Computation time varies greatly.
The quality of the local optimal solution is not very different between the two approaches.
When this algorithm is actually used, it will be checked by a person in the end.
there may be possibilities that obtaining a solution with a certain degree of quality in a short time may be sufficient.

## Slide 61: Manhattan distance
For vectors x and y, we define the Manhattan distance as follows.

## Slide 62: Example of Manhattan distance
We consider the following conditions
  The number of orders is 3 and the number of holds is 4.
  Each order contains 100 vehicles.
The values of the vectors take a small number between 0 and 1.
  the value is 1 when allocating 100% of the order
  the value is 0.5 when allocating 50% of the order

## Slide 63: Example of Manhattan distance
We consider the situation that each order contains
100 vehicles.
→
we convert the values as shown in this table.
order
hold
 | 1 | 2 | 3 | 4
A | 30 | 70 | 0 | 0
B | 0 | 0 | 100 | 0
C | 10 | 10 | 0 | 80
 | 1 | 2 | 3 | 4
A | 0.3 | 0.7 | 0 | 0
B | 0 | 0 | 1.0 | 0
C | 0.1 | 0.1 | 0 | 0.8

## Slide 64: Example of Manhattan distance
Pattern 1
Pattern 2
1.6
0
0.4
1.6
0
0.4
 | 1 | 2 | 3 | 4
A | 0.3 | 0.7 | 0 | 0
B | 0 | 0 | 1.0 | 0
C | 0.1 | 0.1 | 0 | 0.8
 | 1 | 2 | 3 | 4
A | 0.2 | 0 | 0.8 | 0
B | 0 | 0 | 1.0 | 0
C | 0.2 | 0.2 | 0 | 0.6
|0.3-0.2|+|0.7-0|+|0-0.8|
Total distance: 2.0
For each order i, The sum of would be 1.0 and The maximum total distance will be twice the number of orders.
By dividing by twice the number of orders, we can see how different the solutions are.
(In this case, 33%)

## Slide 65: Result of Manhattan distance
orders | L ports | D ports | Difference(%)
38 | 2 | 3 | 0.19
63 | 2 | 3 | 3.57
57 | 2 | 5 | 1.07
66 | 4 | 3 | 0.71
We performed the comparison only on instances for which we had the exact best solution.
We confirmed that the properties of the relaxed solution and the MIP solution are close for all instances.

## Slide 66: Rounding the relaxed solution
For every orders, the value of the variable assigned to the hold is used as a probability to randomly determine which hold to assign to.
If the capacity constraint of the hold is not satisfied, we will not assign orders to that hold.
Hold | Value of the relaxed solution.
A | 0.2
B | 0.5
C | 0.3
Hold | Probability that orders are assigned
A | 20%
B | 50%
C | 30%