## Slide 1: A mathematical modeling for the stowage planning problem
Kiyoshi, TAKEDA
Yagiura lab

## Slide 2: Outline
Background
Problem definition
Modeling
Different modeling
future work

## Slide 3: Background
A carrier ship carries various loads through some ports.
We consider the ship that carries various type of cars. (e.g. passenger car, truck, bulldozer...)
Assignment of cars to ship is planned manually.
We aim to make assignment automatically

## Slide 4: Background
There are a lot of things that has to be considered
  Planning assignments that makes it easy to load and unload cars is important.
  Human error should not happen.
  Unbalanced assignments may result in a sinking.

## Slide 5: Problem Definition
We consider the ships which has 12 decks(floors).
Each deck has up to 4 holds
４
３
２
１

## Slide 6: Given definition
Order information

## Slide 7: Given information
Ship information
  How many holds exist.
  How large each hold is.
  Which holds are connected.
  etc…

## Slide 8: Stowage plan
We assign cars in every order to the hold.
  The order ID 0 is assigned the 3rd hold of 1st deck.
  The order ID 5 is assigned the 2rd hold of 4th deck.

## Slide 9: Mathematical Modeling
We model this assignment based on interviews with planners.
I and Mr.Ukawa made model for this assignment last year.
I will explain objective function and constraints one by one.

## Slide 10: The objective function
the objective function would be the weighted sum of the following five.
avoiding multiple orders in one hold
placing same orders by port closer together
securing a path to prevent loss of work efficiency
No dead space
placing empty space close to the entrance

## Slide 11: avoiding multiple orders in one hold
When an order is unloaded from a hold at a certain port, if there are several orders with different destinations in the same hold, human error may occur.
we minimize the number of orders with different destinations in different loading areas for each hold.
e.g. when unloading at port A
Port A
Port B
Port C
We add a penalty of two to the objective function

## Slide 12: placing same orders by port closer together
it is easy to load and unload cars if same orders by port are placed closer.
we minimize the number of orders with different ports that exist in adjacent pairs of holds.
        ○ ×
Port A
Port B
Port C

## Slide 13: placing same orders by port closer together
As pair of adjacent holds, we consider two patterns
  Adjacent hold to the other
  Holds connected with a slope
We calculate the penalty for both loading ports and destination port
The penalty is 2
The penalty is 7

## Slide 14: Securing a path to prevent loss of work efficiency
When a hold is full, it would be harder to pass through that hold.
The crew need to move cars in that hold once and bring them back again.
This leads to a loss of work efficiency.

## Slide 15: Securing a path to prevent loss of work efficiency
For each hold 𝑖, we defined a filling rate that does not narrow the aisle of the car.
When loading 10 cars to hold 4:
  Red: the hold which the filling rate is exceeded.
  Blue: the hold which the filling rate is not exceeded.
Total penalty for this situation is 20 (10 *2)
1
2
3
4

## Slide 16: No dead space
There are some holds with a ramp connecting the deck to the deck.
Once these holds are filled to a certain extent, it will be impossible to reach the deeper holds.
  This space is called “dead space”
We minimize the number of dead space.
90% full
60% full
50% full
60% full
These space are called dead space

## Slide 17: placing empty space close to the entrance
It often happens that orders are added just before the voyage.
To handle that situation, we should place empty space close to the entrance
The entrance

## Slide 18: placing empty space close to the entrance
The ship has 12 floors and the entrance is on the 5th floor.
If there are lots of empty space in the 5th floor’s holds, we get more profit.
We subtract that profit from the objective function.

## Slide 19: Constraints
Travel routes in the ship
Weight balance of cargo
Height of the hold

## Slide 20: Travel paths in the ship
we secure a path for cars to be able to pass.
For each hold i, we define
  the current filling rate as
  the maximum filling rate that a car can pass as
for every hold that becomes a path through,

## Slide 21: Weight balance of cargo
When the ship tilts, there is a possibility that the ship will lose its balance and roll over.
we add constraints for balance in two directions
  Forward and backward direction
  Vertical direction

## Slide 22: Forward and backward direction
For each hold 𝑖, we define a coefficient
  Positive coefficient from center to forward hold
  negative coefficient from center to back hold
The closer the center of gravity is to zero in the forward and backward directions, the more stable the ship will be.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 23: Vertical direction
For each hold 𝑖, we define a coefficient
  Positive coefficient for the hold above sea level
  Positive coefficient for the hold below sea level
The farther away from the sea surface, the greater the effect is.
Let be the weight of a car in each order 𝑗, does not exceed the threshold.

## Slide 24: Computational experiment
With this model, we confirmed that we can get a good assignment for small bookings.
The number of orders and the number of loading and unloading ports increases, the calculations may not be sufficiently advanced in a limited time.[1]
[1]鵜川知哉, 自動車運搬船における貨物積載プラン ニングの席割問題に対する数理モデリング, 修士 論文，名古屋大学情報学研究科, 2020

## Slide 25: Different model
We create different model to solve large bookings.
We'll call this model “the 2nd model”.
The basic idea is based on heuristics.
Using the local search, we improve the assignment

## Slide 26: Detailed Heuristic
In the proposed mathematical model, continuous numbers of units were used as variables.
In the 2nd model, instead of assigning each unit individually, we split the orders and assign them.
As for holds, we think about grouping some holds together and assigning orders to them.
  We call them “segment”.

## Slide 27: Detailed Segment
The ship has 43 holds.
We divide them into 17 segments.
It is based on the rule that on each floor, planners assign the cars in order from the back hold to the hold with the ramp.
this grouping enable the model to create assignment that is similar to planners'.

## Slide 28: Detailed Segment
→

## Slide 29: Comparison
Example of previous model
assigning 35 vehicles of order 1 to 3rd hold of 4th deck.
same as real operations.
Example of Heuristic model
Assigning order 1 to 3rd segment
Once assignments are decided, we load vehicles from the back according to the rules.

## Slide 30: Rules for loading vehicles
The vehicles of the orders assigned to each segment are loaded from the back hold.
We want to load the vehicle while satisfying the constraints.

## Slide 31: Constraints that has to be satisfied when loading
We load vehicles while satisfying the following the travel routes constraints.
  We ensure that the filling rate is not exceeded after all vehicles have been loaded at a particular port.
Any constraints or objectives other than the above two are considered in the evaluation function.

## Slide 32: Local Search
moving from solution to solution in the space of candidate solutions by applying local changes
We repeat until the termination condition is satisfied
In this research, we use shift and swap neighborhood

## Slide 33: Neighborhood
Shift neighborhood
  This is obtained by reassigning one order which was assigned to a segment to another segment
Swap neighborhood
  This is obtained by swapping the allocated segments of two orders.

## Slide 34: Flow of local search
searching the shift neighborhood until no better solution is found.
searching the swap neighborhood until no better solution is found.
If better solution is found in step 1 or step 2, return to step 1.

## Slide 35: Current situation of implementation
I finished implementing the model that considers all the constraints and objective functions.
We compare the computation time and the quality of assignment.
For 1st model, I show the values of the solution after 1 hour and after 24 hours
For 2nd model, I show the value of the solution and the computation time to finish the local search.

## Slide 36: Computational experiment
 |  |  | 1st model |  | 2nd model | 
Num of orders | Num of loading ports | Num of destination ports | Value after 1h (3600s) | Value after 24h (86400s) | Value | Computation time (seconds)
109 | 2 | 3 | -508 | -3478 | -2959 | 739
109 | 2 | 5 | -2612 | -3354 | -2057 | 653
109 | 4 | 3 | 1240 | -3455 | -630 | 548
200 | 2 | 3 | none | -840 | 6098 | 535
250 | 2 | 3 | none | -2064 | -1867 | 1101
350 | 2 | 3 | none | 3726 | 5198 | 21863

## Slide 37: Summary &future work
Summary
  We confirmed that we can get good solutions for small bookings.
  We proposed heuristic model to solve large bookings.
  For simple models, we confirmed that the computation time can be reduced
Future work
  Implementing the program
  Proposing an approach to find the global optimal solution.